## Slide 1
Design and Simulation of a Digital Access Card Verification System
Digital Logic Design & Hardware Simulation Presentation
2620030622
GADDAM YASWANTH RATHAN
2620030634
RAJANNAGARI VARUN REDDY
2620030641
KATTULA NAGA VEERA VENKATA SAI MANIKANTA
2620030646
GOLI MITHRA REDDY

## Slide 2
Project Goal: Build a secure hardware-based access verification system using pure digital logic and sequential state machines.
Core Mechanism: Instantly compares card credentials and PIN inputs with secure register values.
Simulation Suite: Fully simulated and verified using Logisim for real-time propagation testing.
Reliability: Integrates multi-factor authentication, automatic lockout counters, and visual LED feedback.
Abstract

## Slide 3
Security Risks
Conventional physical keys and basic entry methods lack modern cryptographic logs, secure validation states, and brute-force protection.
System Latency
Microcontroller or OS-based access terminals suffer from boot delays, kernel overhead, and processing bottlenecks during heavy traffic hours.
Robust Logic Need
Necessity for a high-speed, fault-tolerant hardware pipeline capable of handling parallel ID lookups, retry penalties, and instant alarm triggers.
Problem Definition

## Slide 4
Input Stage: Multiplexed switches and keypad inputs mapping card identification bits.
Comparator Array: Bitwise XNOR and AND gate networks evaluating user inputs against master registers.
Control FSM: Finite State Machine managing idle, access granted, and lockout penalties.
Actuation Output: Solenoid driver triggers paired with green/red verification LEDs and buzzers.
Design and Methodology

## Slide 5
Combinational Sub-circuits
Custom 4-bit and 8-bit magnitude comparators designed with primitive logic gates for high-speed verification.
Sequential Registers
D flip-flops and binary adders configured to track incorrect attempts and manage strict lockout cooldown cycles.
Logisim Design

## Slide 6
Circuit Module | Logisim Component | Operational Role
ID Matcher | XNOR Gates & Bitwise AND | Performs bit-by-bit verification against stored master card code.
Error Counter | Registers & Adder Circuits | Monitors consecutive failed entries to enforce security lockouts.
State Controller | Finite State Machine (FSM) | Controls seamless transitions between Ready, Verified, and Alarm states.
Feedback Indicators | LED Matrix & Hex Displays | Provides instant visual status for authorized access or security alerts.
Logisim Implementation

## Slide 7
Valid Entry Test: Instantaneous HIGH logic signal on Green LED upon correct card ID match.
Invalid Entry Test: Triggers Red LED warning and increments the internal failure register.
Lockout Enforcement: Successfully locks entry after 3 consecutive failures for a preset duration.
Propagation Timing: Total gate propagation delay measured well below safe threshold limits.
Simulation and Results

## Slide 8
Hardware Efficiency
Proved that secure access control systems can be built efficiently using pure digital hardware logic without microcontroller reliance.
Robust Simulation
Logisim served as a powerful educational platform for validating complex gate-level connections and state transitions.
Future Scope
Readily scalable to FPGA hardware boards using VHDL/Verilog for real-world deployment and biometric integration.
Conclusion and Key Takeaways

## Slide 9
Thank You
Digital Logic Design & Hardware Simulation Project